## Slide 1: NTCIP Testing Workshop
Part 2
September 5, 2024

## Slide 2: Agenda
Anti-trust and Patent Disclosure
Introduction of participants
Overview of state of the practice
Identified challenges
Introduction of workshop topics
Initial discussion of first 3 topics

## Slide 3: Anti-Trust Guidance
The Institute of Transportation Engineers is committed to compliance with antitrust laws and all meetings will be conducted in strict compliance with these antitrust guidelines. Further if an item comes up for which you have conflict of interest, please declare that you have a conflict of interest on the matter and recuse yourself from action on that item.
The following discussions and/or exchanges of information by or among competitors concerning are prohibited:
  Prices, price changes, price quotations, pricing policies, discounts, payment terms, credit, allowances or terms or conditions of sale;
  Profits, profit margins or cost data;
  Market shares, sales territories or markets;
  The allocation of customer territories;
  Selection, rejection or termination of customers or suppliers;
  Restricting the territory or markets in which a company may sell services or products;
  Restricting the customers to whom a company may sell;
  Unreasonable restrictions on the development or use of technologies; or
  Any matter which is inconsistent with the proposition that each company must exercise its independent business judgement in pricing its service or products, dealing with its customers and suppliers and choosing the markets in which it will compete.

## Slide 4: NTCIP Patent Disclosure Policy
Intellectual Property and Standards
  Participants in the development of Standards, as well as the users of Standards, may have an interest in knowing whether there are provisions in a Standard incorporating someone’s intellectual property, which may require permission to use someone’s proprietary technology and possibly pay compensation for that privilege. The policies of NEMA and ANSI, as well as international Standards organizations, recognize that it is permissible to draft a Standard that includes the use of someone’s patent claims if technical reasons justify it, but Standards developing committees may prefer to avoid incorporating proprietary technology once they know of it.
  The primary concern of these policies is the identification of essential patent claims. NEMA has defined an essential patent as a claim contained in a patent or published patent application, the use of which is necessary to create a compliant implementation of a mandatory provision in the normative clauses of a NEMA Standard or proposed NEMA Standard when there is no commercially and technically feasible non-infringing alternative. Participants in the NEMA Standards developing process are obligated to disclose essential patent claims of which they have knowledge. A participant may self-disclose any essential patent claims they or their employer own or control, or a participant may ask NEMA to query whether another participant or third-party owns or controls any essential patent claims. The obligation to disclose is a continuing one, both before and after a Standard is published.
  Disclosure must identify the patent or patent application, the part of the NEMA Standard incorporating an essential patent claim, and an assurance that a license to use the essential patent claims will be made available either on reasonable terms and conditions that are demonstrably free of any unfair discrimination or without compensation but with other reasonable terms and conditions that are demonstrably free of unfair discrimination.

## Slide 5: Welcome
Remarks from USDOT
Remarks from SDOs

## Slide 6: Introduction of Participants
To respect the time limits of the 2-hour web meeting
  Make sure your name and organization are reflected in your Zoom name
    e.g., Ken Vaughn (Trevilon)
    You can right-click on your icon and select rename to change your Zoom name
  Use the chat window
    If you have specific goals for this worksop series, please type them into the chat window
Notes: If we have fewer than 20 participants, we can perhaps allow introductions; although in that case, I suspect everyone will know each other anyway. It might be best to defer formal introductions to the in-person meetings

## Slide 7: Summary of Workshop Part 1
We reviewed the current state of the practice and posed 7 key questions:
Where should NTCIP test procedures be documented?
Where should ISO 26048-1 test procedures be documented?
How should test procedures be maintained?
What format/language should be used to document procedures?
How detailed should test procedures be?
  Dialog vs functional
  Extent of negative testing
  Level of testing needed (e.g., for acceptance or for security certificate)
  Does each version update of an implementation needs to go through separate testing
What tools are necessary to achieve objectives?

## Slide 8: Summary of Workshop Part 1
We reached consensus on answers to the first 2 questions:
Where should NTCIP test procedures be documented?
  Replace Annex C within each standard with a reference to an external source (including introduction, test case specification, and test procedures)
  The external source should be version controlled
    Approved versions need to be identifiable and unchangeable
    Changes between selected versions should be obtainable
    The approval process should perhaps be conducted by technical experts (e.g., registered users of the site) rather than the traditional industry ballot
    The procedures for all devices should perhaps be the same even though some devices (e.g., CV devices) are likely to undergo testing for formal certification
    No clear requirement for but no objection to a public open-source development environment (e.g., GitHub)
    Having a single file (e.g., PDF) might be useful to refering to the test specifications but this could be developed from separately managed files documenting the details (e.g., one file for each procedure)

## Slide 9: Summary of Workshop Part 1
Where should ISO 26048-1 test procedures be documented?
  Same as for NTCIP (i.e., co-located on the same NTCIP resource)

## Slide 10: How should Test Procedures be Maintained
Status quo
Update with each update of the standard; static document otherwise
Allow online comments
Establish a forum where questions and proposals can be made
Allow online interaction
Establish a forum where questions and proposals can be made and a maintenance team can provide answers/advice
Open source development
Use an online tool (e.g., Github) to manage and approve multiple submitters in making specific edits
If we choose this, what are the details of the process?

## Slide 11: What format/language should be used? NTCIP 8007

## Slide 12: What format/language should be used? Structured English – e.g., NTCIP 8007 without the table format
Configure the following parameters:
»Required_Max_Pages
GET the following object(s):
»dmsMaxNumberPages.0
IF get succeeds
“PASS”
ELSE
“FAIL” and exit
IF RESPONSE VALUE for dmsMaxNumberPages.0 is greater than or equal to Required_Max_Pages
“PASS”
ELSE
“FAIL” and exit

## Slide 13: What format/language should be used? Pseudocode
procedure DetermineMaxPages () {
// Step 1
requiredMaxPages = get “Required_Max_Pages” from configuration file;
// Step 2
response = snmp_get(dmsMaxNumberPages.0);
if (response == noError) {
print “Pass”;
} else {
print “Fail” with backtrace;
exit;
}
// Step 3
if (dmsMaxNumberPages.0 >= requiredMaxPages) {
print “Pass”;
} else {
print “Fail”;
throw exception;
}
}

## Slide 14: What format/language should be used? XML structure
<test-case>
<name>Determine Maximum Number of Pages</name>
<steps>
<CONFIGURE>
<variable>
<name>Required_Max_Pages</name>
<format>ofDecimal</format>
<minimum>1</minimum>
<maximum>255</maximum>
<default>3</default>
</variable>
</CONFIGURE>
<GET>
<variable>
<name>dmsMaxNumberPages.0</name>
<format>ofDecimal</format>
</variable>
</GET>
<VERIFY>
<comparison>
<value1>dmsMaxNumberPages.0</value1>
<operator>exOpGreaterEqual</operator>
<value2>Required_Max_Pages</value2>
</comparison>
</VERIFY>
</steps>
</test-case>

## Slide 15: What format/language should be used? C++
CTest CSuiteDMS::DetermineMaxPages() {
CPacket response;
CPacket request;
CTest test;
// Step 1: CONFIGURE Required_Max_Pages
CVariable requiredMaxPages = findVariable( "Required_Max_Pages" );
if (requiredMaxPages == NULL) {
test->addStep("1", "Required_Max_Pages", "Variable not found", TEST_FAIL);
return test;
}
test->addStep("1", "Required_Max_Pages", requiredMaxPages.getValueString());
// Step 2: GET dmsMaxNumberPages.0
request.Clear();
request.AddObjectByName("dmsMaxNumberPages.0");
step = snmpGet(request, response, 1);
test->addStep(step);
if (response.GetType() == SNMP_CLASS_TIMEOUT)
return test;
// Step 3: VERIFY dmsMaxNumberPages.0 >= Required_Max_Pages
if (response.getObjectValueInt(0) >= requiredMaxPages.getValueInt()) {
test->addStep("3", "dmsMaxNumberPages.0 >= Required_Max_Pages", "Pass", TEST_PASS);
} else {
test->addStep("3", "dmsMaxNumberPages.0 >= Required_Max_Pages", "Fail", TEST_FAIL);
}
return test;
}

## Slide 16: What format/language should be used? JavaScript
class CSuiteDMS {
determineMaxPages() {
const response = new CPacket();
const request = new CPacket();
const test = new CTest();
// Step 1: CONFIGURE Required_Max_Pages
const requiredMaxPages = findVariable("Required_Max_Pages");
if (!requiredMaxPages) {
test.addStep("1", "Required_Max_Pages", "Variable not found", "TEST_FAIL");
return test;
}
test.addStep("1", "Required_Max_Pages", requiredMaxPages.getValueString());
// Step 2: GET dmsMaxNumberPages.0
request.clear();
request.addObjectByName("dmsMaxNumberPages.0");
const step = snmpGet(request, response, 1);
test.addStep(step);
if (response.getType() === "SNMP_CLASS_TIMEOUT") {
return test;
}
// Step 3: VERIFY dmsMaxNumberPages.0 >= Required_Max_Pages
if (response.getObjectValueInt(0) >= requiredMaxPages.getValueInt()) {
test.addStep("3", "dmsMaxNumberPages.0 >= Required_Max_Pages", "Pass", "TEST_PASS");
} else {
test.addStep("3", "dmsMaxNumberPages.0 >= Required_Max_Pages", "Fail", "TEST_FAIL");
}
return test;
}
}

## Slide 17: What format/language should be used? Python
def determine_max_pages(self):
response = CPacket()
request = CPacket()
test = CTest()
# Step 1: CONFIGURE Required_Max_Pages
required_max_pages = find_variable("Required_Max_Pages")
if not required_max_pages:
test.add_step("1", "Required_Max_Pages", "Variable not found", "TEST_FAIL")
return test
test.add_step("1", "Required_Max_Pages", required_max_pages.get_value_string())
# Step 2: GET dmsMaxNumberPages.0
request.clear()
request.add_object_by_name("dmsMaxNumberPages.0")
step = snmp_get(request, response, 1)
test.add_step(step)
if response.get_type() == "SNMP_CLASS_TIMEOUT":
return test
# Step 3: VERIFY dmsMaxNumberPages.0 >= Required_Max_Pages
if response.get_object_value_int(0) >= required_max_pages.get_value_int():
test.add_step("3", "dmsMaxNumberPages.0 >= Required_Max_Pages", "Pass", "TEST_PASS")
else:
test.add_step("3", "dmsMaxNumberPages.0 >= Required_Max_Pages", "Fail", "TEST_FAIL")
return test

## Slide 18: What format/language should be used? Tcl
proc determineMaxPages {} {
# Placeholder objects for response and request packets
set response [dict create]
set request [dict create]
set test [list] ;# Simulate the test object as a list of steps
# Step 1: CONFIGURE Required_Max_Pages
set requiredMaxPages [findVariable "Required_Max_Pages"]
if {$requiredMaxPages eq ""} {
lappend test [list "1" "Required_Max_Pages" "Variable not found" "TEST_FAIL"]
return $test
}
lappend test [list "1" "Required_Max_Pages" $requiredMaxPages]
# Step 2: GET dmsMaxNumberPages.0
dict set request "Clear" ""
dict set request "AddObjectByName" "dmsMaxNumberPages.0"
set step [snmpGet $request response 1]
lappend test $step
if {[dict get $response "GetType"] eq "SNMP_CLASS_TIMEOUT"} {
return $test
}
# Step 3: VERIFY dmsMaxNumberPages.0 >= Required_Max_Pages
set responseValue [dict get $response "getObjectValueInt" 0]
set requiredMaxPagesValue $requiredMaxPages ;# Adjust if needed to extract the value correctly
if {$responseValue >= $requiredMaxPagesValue} {
lappend test [list "3" "dmsMaxNumberPages.0 >= Required_Max_Pages" "Pass" "TEST_PASS"]
} else {
lappend test [list "3" "dmsMaxNumberPages.0 >= Required_Max_Pages" "Fail" "TEST_FAIL"]
}
return $test
}

## Slide 19: Comparison of Formats
Format | Readability | Portability | Versioning | Compilability | Acceptability | ???
Table | 8 | 2 | 2 | 0 |  | 
Struct English | 7 | 3 | 9 | 0 |  | 
Pseudocode | 5 | 4 | 9 | 0 |  | 
XML | 3 | 9 | 9 | 5 |  | 
C++ | 4 | 8 | 9 | 10 |  | 
Javascript | 4 | 8 | 9 | 10 |  | 
Python | 4 | 8 | 9 | 10 |  | 
TCL | 4 | 8 | 9 | 10 |  | 

## Slide 20: How detailed Should Test Procedures Be?
Dialog versus functional
Extent of negative testing
Level of testing needed (e.g., for acceptance or for security certificate)
Does each version update of an implementation needs to go through separate testing

## Slide 21: What tools are necessary to achieve objectives?
GitHub?
Compilers?
SNMPv3 Test Tools?
Traceability Tools?

## Slide 22: Preparations for an In-person meeting
Main Agenda Items
  Finishing Questions
  Feedback from Prototype Environment
Who is likely to attend in person? (Show of hands)
Should we try to co-locate with another event?
  Oct 21-25: ISO TC 204 Plenary, Cambridge, MA
  Oct 28: Plugfest. San Diego, CA
  Nov 13-15: Texas District ITE, Houston, TX
  Dec 10-12: ISO TC 204 WG 19, Raleigh, NC (Tentative)
  Jan 5-9: TRB, Washington, DC
  Others?

## Slide 23: Backup Materials

## Slide 24: State of the Practice for NTCIP Testing
Test procedures are written to conform to NTCIP 8007
NTCIP 8007 is being updated to support SNMPv3
We could redefine the format completely

## Slide 25: State of the Practice for NTCIP Testing
Test procedures are documented in Annex C of device-specific standards
  Only included in 1203 (message signs) and 1204 (weather stations) currently
    Based on NTCIP functional testing (i.e., testing to meet NTCIP functional requirements)
  Being added to 1202 (traffic signals)
    Focused on NTCIP dialog testing (i.e., testing against standard dialogs only)
Test procedures double the size of the standards
Tests for global objects are largely duplicated among these documents
For 1203 and 1204 many agencies require the manufacturer to show proof of testing
  Many agencies seem to test against either their central software or a special testing program based on their central software and do not use official test procedures
  There may be other agencies that require some proof of acceptance testing within perhaps the latest version of the NTCIP standards
    Testing does not seem to be required for new software versions. Different models may be retested in some cases depending on agency
  Most of the testing seems to be done by a small number of entities

## Slide 26: Challenges
Documenting test procedures in the standard delays publication of updates
  Twice as much text to develop, maintain, and review
  Little indication that the test procedures are actually reviewed by industry
Written test procedures are a type of pseudo code and should be tested
  "untested code is usually incorrect” 1
  Having errors in a normative Annex of the main standard creates potential conflicts with the body of the standard
The current test procedure format is not directly implementable
  Each test agency expends considerable effort in translating into their own code and often requires interpretations to correct errors
  Minor maintenance changes to the test procedures are easily overlooked (i.e., it is not directly transferable to code because it is not perfect)
  There is no mechanism for implementers to report errors or for corrections to be continually captured to evolve the code
  Any time a programmer touches code, thre is a high probability that something will break and regression testing is needed
Procedures for the ATC API were written in XML so that tools could use it; there are perhaps benefits of using a consistent approach
1 Lamport, Leslie (2 January 2009). "The PlusCal Algorithm Language" (PDF). Microsoft Research. Retrieved 28 May 2024.

## Slide 27: Challenges – No consensus on Level of Testing
Extent of testing within procedures
  Object-level: Does the device allow reading (writing) of each object for values within the range
    Advantage: Can be completely automated based on the object SYNTAX and ACCESS
    Challenge: Some objects have special semantics that inhibit this type of testing
    Example: Can I set the yellow clearance interval to any value in its defined range?
  Dialog-level: Does the device allow a management station to perform the standardized dialogs
    Advantage: Somewhat automated, while addressing the complications due to semantics
    Challenge: Does not verify that the operation/status of the device reflects the NTCIP information per NTCIP functional requirements and does not reveal many of the potential differences in manufacturer’s interpretations
    Used for Anaheim testing
    Example: Can I download a new timing plan?
  Data Interaction level
  NTCIP functional-level: Does the device conform to the functional requirements of the standard
    Advantage: Provides verification of the stated requirements
    Challenge: Much more labor intensive , more difficult to develop and create test scenarios, and still does not test for all complications (e.g., multiple stress conditions at once)
    Example: Does the device properly implement a newly downloaded timing plan?
  Full NTCIP testing: Does the device conform to all real-world requirements and satisfy user needs
    Advantge: The gold standard
    More labor intensive, more difficult to develop and create test scenarios
    Example: Does the device properly recover when power is lost during the middle of a timing plan download

## Slide 28: Challenges – No consensus on Level of Testing
Extent of testing among test cases
  Everyone agrees on test procedures for positive testing
    Verifies that the device responds properly to proper requests
    Has a clearly defined scope
  Little guidance on how much negative testing
    Verifies that the device correctly rejects and recovers from improper requests
    Has a very open-ended scope with no guidance or consensus on level of testing needed
Extent of testing implementations
  Do agencies understand what another agency’ approval means
  What should be required to receive 1609.2 security or other credentials
    Testing of each unit
    Testing of each software version
    Testing of each model
    Testing of each manufacturer
    Etc.

## Slide 29: Challenges
Developing test procedures is labor intensive
Performing test procedures is labor intensive
Level of effort tends to be exponential to the type of testing (in layman’s terms), for example:
  Object-level = 1 hour
  Dialog-level = 1 day
  NTCIP functional-level = 2 weeks
  Full = months or years
  Factors likely increase with device interface complexity
Level of effort can potentially be offset by automation
  Automating different aspects entails its own development costs

## Slide 30: Challenges
Different testing agencies use different test software
  Each tool uses a different scripting language
Migrating to SNMPv3 will require updating all test procedures
  Some revisions are simple but on whole, a large percentage of the objects have been revised
Need to consider appropriate test procedures for security
  e.g., testing the requirements of ISO 15784-2, such as ensuring that the firewall works
Version control of test procedures, especially when a device supports multiple standards that are updated at different frequencies
Opportunity
AI tools should be able to translate between scripting languages fairly easily

## Slide 31: Key Questions For Our Workshop Feel Free to Propose Additional Issues in the Chat Window
Where should NTCIP test procedures be documented?
Where should ISO 26048-1 test procedures be documented?
How should test procedures be maintained?
What format/language should be used to document procedures?
How detailed should test procedures be?
  Dialog vs functional
  Extent of negative testing
  Level of testing needed (e.g., for acceptance or for security certificate)
What tools are necessary to achieve objectives?
Does each version update of an implementation needs to go through separate testing

## Slide 32: Where to Document NTCIP Test Procedures?
Keep all documentation in Annex C as done currently
Keep introduction, Req-TC traceability table, and test cases in Annex C but reference external source for procedures
Keep introduction and Req-TC traceability table in Annex C but reference external source for test cases and procedures
Keep introduction in Annex C but reference external source for everything else
Replace Annex C with a simple reference for all test documentation (test specification should be version controlled such that redline versions of changes can be obtained)
No need for industry-wide test procedures
NOTE: The introduction currently defines:
  The scope of test procedures
  The format used for test procedures
  Rules for executing test procedures, and
  The test environment

## Slide 33: Where to Document NTCIP Test Procedures? If we remove conent from Annex C
Does the industry need the remaining content to be “standardized” through some ballot process?
  Perhaps a “standard” release approved by technical experts rather than traditional industry ballot – for consideration by NTCIP JC and others
  Perhaps the test procedures are developed and approved through a similar process for all devices but only CV devices are required to go through a formal certification process
What final format(s) is/are most useful for the industry, e.g.,
  +1 A document (e.g., PDF)
  A website (e.g., providing bi-directional hyperlinks into a copy of the standard)
  A single parseable electronic file (e.g., source code, json, etc)
  A set of parseable electronic files
  A combination (e.g., a website for traceability with links to electronic files for the script for each test case)
  Unclear, but one approach might be to develop individual files for each test case and a program that combines all of the individual files into a final single PDF per device.
Does the industry need access to interim versions under development?
  For example, if there are bug fixes or other improvements, does the industry need to wait for the reballot period?
  No strong feeling at present, not objections to using GitHub for access to interim versions with open-source philosophy

## Slide 34: Where to Document ISO 26048-1 Test Procedures?
Same as for NTCIP but in an ISO-managed resource
Same as for NTCIP and in a NTCIP managed resource
Same as for NTCIP but public domain (e.g., USDOT specification)
Duplicated within each NTCIP device-specic resource
Other?